## Slide 1
Passive Front End Redesign
The Logicals
Tiffany Morisak, Robert Wilhelm, Jason Korchuk, Cody Hutchins, April Freier
Sponsor: RTLogic—John Wiley
Faculty Sponsor: Dr. Darshika G Perera
2/24/17

## Slide 2: Team
  Cody Hutchins (Computer Engineer—Team Lead)
  April Freier (Computer Engineer—Software Design)
  Jason Korchuk (Computer Engineer—Circuit Modeling)
  Robert Wilhelm (Electrical Engineer—Circuit Assembly)
  Tiffany Morisak (Electrical Engineer—Circuit Modeling)

## Slide 3: Introduction
Review: Specification
Proposed Solutions: Considerations
Literature Search
PCB Design
Design Progress
Test Plan
Demonstration Plan
Timeline
Budget
Conclusion

## Slide 4
Inside Scope
Connects to Script
Inputs
Signal Switch
Signal Pad
Signal Splitter
Received and Transmitted Signals from RF Down Converter Box
Switches between received and transmitted signals using 5 V signals
Pad maintains 50 Ohm impedance but causes 4 DB loss
Splits signal and maintains impedance for ADC analyzation
All further signal processing for this project takes place in in script

## Slide 5: Design Sections
Input Frequency Upgrade
Operating Temp Verification
Calibration Script Upgrade

## Slide 6: Current Specifications
Specification | Value | Requirements
Input Frequency | 850 MHz to 2500 MHz | 850 MHz to 6000 MHz
Instantaneous Bandwidth | 54 MHz | 54 MHz
Typical Operating Input Power | -65 dBm to -25 dBm | -65 dBm to -25 dBm
Gain Stability Over 24 hours | ± 0.25 dB Over 24 hours at 25° C | ± 0.25 dB Over 24 hours at 25° C
Operating Temperature | 0° C to 50° C | 0° C to 50° C
Power | 500 mA@5V, 900 mA@3.3V, 50 mA@12V | 500 mA@5V, 900 mA@3.3V, 50 mA@12V
Size | 7.72”/5.65”/1.22” | 7.72”/5.65”/1.22”
AC Supply | 100-200V AC, 50/60 Hz | 100-200V AC, 50/60 Hz
DC Output | 20W Maximum | 20W Maximum

## Slide 7: Temperature Performance
Thermotron 2800
Per RT Logic’s request, current temperature performance of Saturn will be tested.
  Test will give us information on the board’s original operation
Redesign will maintain this performance.

## Slide 8: Environmental Testing Process
Step | Action | Expected Result
1 | Setup Signal Generator CF – 2000 MHz, dBm -40 | Setup
2 | Launch dwell windows on both channels, switch display to frequency domain, continuous sweep | Two channels are displayed, accurately reflecting the signal generator output
3 | Run the Thermotron profile | Data logging is enabled
4 | Record baseline measurements at -50℃, 10-15 minutes into test. | Record log file of power at each frequency.
5 | Repeat Step 4 in 10℃ increments, up to 80℃. | Record log file of power at each frequency.

## Slide 9: Software Design Process
Understand existing scripts
Determine what SPARQL does
Change SPARQL to SCPI
Testbed Setup
New Calibration Script Development

## Slide 10: Calibration Scripts
Two scripts used to connect to the Saturn board for testing and final configuration in Octave (Matlab Variant)
  First script will run a verification test on the board
  Second script configures data on the board
Transition SPARQL to SCPI considering these points
  Gain
  Attenuation
  DC_tracking
  DC_offset

## Slide 11: SPARQL Example
Subject: Prefix specifies data location on Saturn Board
  HTML file location is the board’s local database
Predicate: “insert” command
Object: Set internal values on system
  Gain, Attenuation, DC_tracking and DC_offset variables

## Slide 12: Option 1: Wider Range Balun
Pro | Con
Similar to current design | Larger PCB footprint
Fewer components needed | Performance drops as bandwidth increases
Lower cost | Few to choose from

## Slide 13: Literature Search: Broadband Balun
Magnetic coupling for <10MHz
Capacitive coupling for 1GHz+
Wire wound transmission line (mag/cap) for 500kHz-10GHz

## Slide 14: Option 2: RF Switch-Multiple Baluns
Pro | Con
Better performance per balun | Much higher cost
More options available | More components on board

## Slide 15: Literature Search: RF Switch
Property | PIN Diode | FET | Hybrid | Electromechanical
Frequency Range | From MHz | From DC | From kHz | From DC
Insertion Loss | Medium | High | High | Low
Roll Off | Low Frequencies | High Frequencies | High Frequencies | N/A
Isolation | High Frequencies | Low Frequencies | High Frequencies | Broad Range
Switching Speed | Fast | Average | Average | Slow
Power Consumption | High | Low | Moderate | Variable
Sensitivity | Temperature | Temperature | Temperature | Vibration

## Slide 16: Goals: Update
Goal 1: Increase Input Range
Goal 2: Set Thermotron Value
Goal 3: Rewrite Scripts with SCPI
Stretch Goal 1: Produce functional PCB of either option
Stretch Goal 2: Retrofit new design to current Saturn board

## Slide 17: Layout of Redesigned PCB
Considered:
  Trace Width
  Trace Length
  Component Orientation
Assistance:
  Bogdan Crivin
  John Wiley

## Slide 18: Departure from Project Requirements
Didn't change many of the requirements, just some very small adjustments

## Slide 19: Design Progress
    PCB layouts completed/Submitted for approval
      Original Layout
      Revised Layout
    Compare PFE test data to simulation output
    SPARQL to SCPI transition nearing completion
    Thermotron Testing Round 1: Complete!

## Slide 20: Design Work Left Before Final
Compare existing script to new and improved script
Send eagle layout to OSHPark
Test the Redesign in the Thermatron
Test new passive front end

## Slide 21: Test Plan
Reproduce Passive Front End (PFE) and compare to full Saturn
  Spice simulations of current components
  Compare Spice simulation to tests taken on Saturn boards
  Build PFE and thermal test with Saturn
Redesign PFE
  Spice simulations of new components
  Compare new Spice output to old Spice output to determine success

## Slide 22: Demonstration Plan: Spice
Simulate frequency sweep at output
  Overlay current dBm plot with test data
    Use Excel to convert from Vout-Iout to dBm
  Overlay new dBm plots with current dBm plots

## Slide 23: Demonstration Plan: Thermal
Thermal Test
  Video of Thermal Chamber testing
Thermotron 2800

## Slide 24: Demonstration Plan: Scripts
SCPI
  Calibration video using new scripts

## Slide 25: Gantt Chart

## Slide 26: Budget (Original)
Item | Quantity | Price | Total Price
PCB Printout | 1 | 25 | 25
Connectors SMA JACK 50 OHM | 4 | 6.24 | 24.96
Resistor 100 OHM | 8 | .1 | .8
Resistor 221 OHM | 8 | .1 | .8
Resistor 23.7 OHM | 4 | .1 | .4
Resistor 93.1 OHM | 4 | .1 | .4
Capacitor 100pF | 28 | .52 | 14.56
IC Switch SPDT | 4 | 3.36 | 14.52
Wound Chip Balun | 4 | .75 | 3
Inductor 1nH | 8 | .75 | .8
 |  |  | 85.24

## Slide 27: Budget (Redesign)
Item | Quantity | Price | Total Price
PCB Printout | 1 | 25 | 25
Connectors SMA JACK 50 OHM | 4 | 6.24 | 24.96
Resistor 100 OHM | 8 | .1 | .8
Resistor 221 OHM | 8 | .1 | .8
Resistor 23.7 OHM | 4 | .1 | .4
Resistor 93.1 OHM | 4 | .1 | .4
Capacitor 100pF | 28 | .52 | 14.56
IC Switch SP2T | 4 | 1.43 | 5.72
High Power Surface Mount Balun | 2 | 124 | 248
Inductor 1nH | 8 | .75 | .8
 |  |  | 321.44

## Slide 28: Conclusion
Review: Specification
Proposed Solutions: Considerations
Literature Search
PCB Design
Design Progress
Test Plan
Demonstration Plan
Timeline
Budget
Conclusion

## Slide 29: Questions